## Slide 1: Introduction to Pollynet_Processing_Chain (Picasso)
Zhenping Yin
2019-07-21
Automate everything
Data Processing Platform
Polly community

## Slide 2: PollyNET
Automated Lidar (PollyXT_LACRO)
Automated Lidar (PollyXT)
PollyNET Data Server
Hours or days
Automated Lidar (PollyXT_TJK)
Automated Lidar (PollyXT_TAU)
Automated Lidar (arielle)

## Slide 3: PollyNET
Automated Lidar (PollyXT)
PollyNET Data Server
automatic program (1st)
Within one hour!!!
1. No quality control
2. No target classification
3. No Housekeeping

## Slide 4: PollyNET
Picasso
Automated Lidar (PollyXT)
PollyNET Data Server
Continuously
UI/polly web
Lidar calibration
depol calibration, water vapor calibration
aerosol extensive and intensive properties
housekeeping, overlap function, …
Within one hour!!!

## Slide 5: Outline
Download and Setup
Hands-on
Concept about Version Control with Git
This introduction will assume you have good knowledge of lidar data retrievals

## Slide 6: Requirements for Running Picasso
Interpreter
MATLAB >= 2014a
Python 3
Python packages: matplotlib, numpy and scipy
Polly Data
Root Dir + pollyType + ‘data_zip’ + yyyymm
Housekeeping data file
Compressed polly data file
Version control
Not necessary but recommended

## Slide 7: Download
One step further…
If you want to develop new features, we recommend you to pull the ‘dev’ branch as well:
git fetch origin dev:dev
(Detailed information about how to play with `git`, please go to ../doc/git_workflow.pptx).
git clone https://github.com/ZPYin/Pollynet_Processing_Chain
This command will download the code from the remote GitHub repository
(There is also ‘download’ option under this link)

## Slide 8: Structure of Picasso
Picasso
figures
results
calibration
log
Unzip polly data
todo_filelist
pollynet_history_of_places_new.txt
pollynet_processing_chain_link.txt
polly config file
polly defaults
Polly processing module
Single task

## Slide 9: Setup
Picasso Global Config
2. edit the global config file
directories: according to your own requirements
‘//’ for windows path separator
to control whether to delete the unzipped polly data after each processing.
python 3 folder: Picasso uses python3 for data visualization if ‘visualizationMode’was set ‘python’
1. setup the global config file from the template (must be renamed as ‘pollynet_processing_chain_config.json’)
Detailed information can be found in
../doc/pollynet_processing_chain_config.pdf

## Slide 10: Setup
Picasso adds campaign:
Normally, this file was generated from the database. But if there is no connection to the database, you need to add new campaign manually.
(Be careful about the character of the ‘space’, actually it consists of ‘tab’. So better way is to copy the line before and then edit it according to your own demands.

## Slide 11: Setup
Picasso adds polly config
Copy the ‘template_config.json’ to a new polly config file with the naming of ‘{polly-type}_config_{date}.json’
You may need to change the settings of:
gdas1Site
AERONETSite
depol_cal_ang_p_time
depol_cal_ang_n_time
meteorDataSource
IWV_instrument
intNProfiles
minIntNProfiles
radiosondeFolder
logbookFile
You can find detailed info about the polly config in /doc/polly_config.md

## Slide 12: Setup
Picasso adds the link between polly config file and polly data
config history file works as a lookup table for Picasso to search the corresponding polly config file.
better way to do is to copy the line before and then edit it according to your demands.
Now, everything is really. Let’s have a try…

## Slide 13: Hands on for running Picasso

## Slide 14: Bash Scripts for automating it

## Slide 15: Add a new campaign
1. New campaign entry
3. New link entry
2. New polly config
pollynet_history_of_places_new.txt
pollynet_processing_chain_link.txt
polly config file
polly defaults
Polly processing module
For simplicity, you can copy the ‘polly_global_config.json’ and rename it according to your requirements.

## Slide 16: Hands on

## Slide 17: Add a new Polly
1. New campaign entry
5. New link entry
4. New polly config
3. New polly defaults
2. New polly modules
pollynet_history_of_places_new.txt
pollynet_processing_chain_link.txt
polly config file
polly defaults
Polly processing module

## Slide 18: Hands on

## Slide 19: Picasso Development
Automatic calibration
  lidar calibration
  water vapor calibration
  depolarization calibration
Integrated conventional retrieving algorithms
Extensible programming structure

## Slide 20: Picasso Development
Requirements:
Be familiar with the whole structure and algorithms
Be professional with MATLAB
Take `PollyXT_LACROS` at Limassol, Cyprus as an example
(Check the polly data first)

## Slide 21: TODO
Full support of data visualization with MATLAB, which can remove the dependence on Python
Uncertainty analysis
Products output (Level 1 (signal correction), Level 2 (calibration results, extensive and intensive properties))
Dual-FOV method for retrieving cloud microphysical properties

## Slide 22: Version Control
Server
Picasso
Dev
User
GitHub

## Slide 23: Version Control
Branch A
Branch B
Branch C

## Slide 24: Hands on
Push to the remote branch
git fetch origin Picasso_intro:Picasso_intro # download the remote branch
git branch # list all the available branches in the repo
git checkout Picasso_intro # navigate to `Picasso_intro`
git status # list all the local changes
git add * # stage all the changes
git commit –m “commit message” # commit message to describe what you’ve done
git push origin Picasso_intro # Push the local changes to the remote branch
Fetch the branch of `Picasso_intro` to your local machine
Add the whole processing function of `arielle`
Add main function
Add function libraries
Add defaults
Setup config and link file

## Slide 25: Backup

## Slide 26: Python user? No problem!
From larda description page
https://martin-rdz.github.io/larda-doc/html/how_to_use.html

## Slide 27: Rayleigh Fit
Range Corrected Signal:
Attenuated molecular backscatter:
In aerosol-free or nearly aerosol-free (quantitatively?) area, assuming ,
Therefore
Main task is to search the most linear correlated area

## Slide 28: Rayleigh Fit
Normalize the measured signal with attenuated molecular backscatter
Test 1: Pure Rayleigh Conditions
Test 3: White-Noise criterion
Test 4: SNR constrain
Test 2: Near and far range cross criteria
if no other absorptive aerosol layers above it
(Baars et al, AMT, 2016)

## Slide 29: Rayleigh Fit
Normalize the measured signal with attenuated molecular backscatter
Test 1: Pure Rayleigh Conditions
Test 2: Near and far range cross criteria
Test 3: White-Noise criterion
Test 4: SNR constrain
Smaller the mean of the residual is and more Gauss distribution alike the residual is, more possible it could be aerosol-free.

## Slide 30: Shortage of sliding fixed window
Omission: This possible interval will not be found if a large fixed window (like 1 km) was used, since the width of aerosol-free area is only 450m.
More computation: all the sub-areas with a fixed width will be tested.

## Slide 31: Rayleigh Fit – area decomposition
Interested area:
Not intersected
Nearly aerosol-free
Which means the slope of the interested area should be 0 and the shape of interested area should be nearly linear

## Slide 32: Rayleigh Fit - Douglas-Peucker Algorithm
Gifs to show how Douglas- Peucker Algorithm works
Each interval is not intersected.
Each interval is nearly linear, but slope of each interval is still varied.

## Slide 33: Rayleigh Fit
Douglas-Peucker Algorithm
[[z_min1, z_max1], [z_min2, z_max2], … [z_mink, z_maxk]]
Test 1: Slope check
Test 2: Near and far range cross criteria
Test 3: White-Noise criterion
Test 4: SNR constrain
Select the best fit ref interval:
(mean value, standard deviation and slope of the residual, mean square root error from a linear regression, test statistic of Anderson-Darling test)